## Slide 1
Conceptual Figures for Paper
Post-Quantum Cryptographic Authentication on C-V2X Mode 4 Sidelink
Draft / Conceptual — For Professor Review
6 figures: System Architecture, SPDU Structure, SPS Flowchart, Intersection Layout, TBS Feasibility, Subchannel Grid

## Slide 2
Fig. 1 — System Architecture
Simulation stack: SUMO ↔ Veins ↔ openCV2X (OMNeT++) with PQC integration
SUMO (Microscopic Traffic Simulator)
• Vehicle mobility • Intersection signal control • 4-leg intersection scenario
Veins (V2X Simulation Framework)
• TraCI interface to SUMO • Channel models (LOS/NLOS) • Mobility coupling
OMNeT++ / openCV2X (Network Simulator)
• LTE sidelink (PC5) • Mode 4 SPS MAC • Full protocol stack
TraCI
INET
Application Layer (Mode4App)
PQC Module (liboqs: Falcon-512, Dilithium-2, ECDSA)
IEEE 1609.2 Security (SPDU: Header + BSM + Signature + Certificate/Digest)
PDCP / RLC
MAC Layer — Mode 4 SPS (LteMacVUeMode4)
SPS: Sensing + Selection Reselection Counter CBR Congestion Ctrl
PHY — LTE Sidelink PC5 (PSCCH + PSSCH)
LOS: Analytical (Dual-slope)
NLOS: Urban Microcell + Nakagami Fading

## Slide 3
Fig. 2 — IEEE 1609.2 SPDU Byte-Level Structure
Comparison of SPDU sizes: ECDSA (compact) vs Falcon-512 (viable) vs Dilithium-2 (infeasible)
ECDSA-256
Hdrs 28B
BSM 39B
Sig 64B
Cert 32B
= 163 B
Falcon-512 (certificate)
Hdrs 28B
BSM 39B
Sig ~660B
Cert (pub 897B + meta) ~967B
= 1694 B
Falcon-512 (digest)
Hdrs 28B
BSM 39B
Sig ~660B
Digest 8B
= 735 B
Dilithium-2 (INFEASIBLE)
Hdrs 28B
BSM 39B
Sig 2420B
Digest 8B
= 2495 B
Max TBS = 2,481 B
■ Headers ■ BSM Payload ■ Signature ■ Certificate/Digest --- Max TBS (MCS 11, 10 SC)

## Slide 4
Fig. 3 — C-V2X Mode 4 Semi-Persistent Scheduling (SPS) Flowchart
Resource selection and reservation procedure per 3GPP TS 36.321 / TS 36.213
BSM Generated at Application Layer (every 100 ms RRI)
Sense Channel: Measure RSSI/RSRP over Sensing Window (1000 ms)
Build Candidate Resource Set (SA) Exclude resources with RSRP > threshold
Randomly Select from Top 20% Lowest Average RSSI Candidates
Create SPS Grant (Fix MCS + Subchannels for reservation)
Transmit SPDU (PSCCH + PSSCH on reserved resources)
Decrement Reselection Counter (initialized to [5, 15])
Counter = 0?
Yes → Reselect
No → Keep with prob. pKeep (0.8)
← New sensing & selection

## Slide 5
Fig. 4 — Intersection Scenario Layout
4-leg signalized intersection with varying vehicle densities (LOS A/C/F)
West (W)
East (E)
North (N)
South (S)
Comm. range (~300 m)
Traffic Density Scenarios
LOS A (Free-flow)
Density: 10 veh/km
Flow: 724 veh/h/approach
LOS C (Stable flow)
Density: 50 veh/km
Flow: 3,622 veh/h/approach
LOS F (Breakdown)
Density: 100 veh/km
Flow: 7,243 veh/h/approach
Parameters: 20 MHz BW, 10 subchannels, MCS 5–11 RRI = 100 ms, Tx power = 23 dBm, 5.9 GHz Turn split: 80% through / 10% left / 10% right

## Slide 6
Fig. 5 — Transport Block Size (TBS) Feasibility Analysis
Can the SPDU fit within the sidelink TBS? (3GPP TS 36.213 lookup tables)
Bytes
MCS 5 (QPSK)
252
504
776
1288
MCS 7 (QPSK)
328
664
1032
1736
MCS 11 (16QAM)
488
984
1544
2481
ECDSA SPDU = 163 B
Falcon-512 Digest = 735 B
Falcon-512 Cert = 1,694 B
Dilithium-2 = 2,495 B
Max TBS = 2,481 B
Dilithium-2: INFEASIBLE (2,495 B > 2,481 B max TBS) Falcon-512: Requires MCS ≥ 10, ≥ 8 subchannels for cert-bearing SPDU

## Slide 7
Fig. 6 — Sidelink Subchannel Allocation per Algorithm
Time-frequency resource grid showing PSCCH + PSSCH occupancy per transmission
ECDSA-256 (163 B)
SC1
SC2
SC3
SC4
SC5
SC6
SC7
SC8
SC9
SC10
PSCCH
PSSCH
SCI
DATA
2/10 subchannels used (20%)
Falcon-512 Digest (735 B)
SC1
SC2
SC3
SC4
SC5
SC6
SC7
SC8
SC9
SC10
PSCCH
PSSCH
SCI
DATA
4/10 subchannels used (40%)
Falcon-512 Cert (1,694 B)
SC1
SC2
SC3
SC4
SC5
SC6
SC7
SC8
SC9
SC10
PSCCH
PSSCH
SCI
DATA
8/10 subchannels used (80%)
■ SCI (Sidelink Control) ■ PSSCH Data □ Unused/Available | Each subchannel = 10 RBs | 20 MHz bandwidth, adjacent scheme
Key Insight: Falcon-512 with full certificate consumes 80% of sidelink resources per TX, leaving only 2 subchannels for other vehicles in the same subframe. ECDSA uses only 20%, enabling 4× more concurrent transmissions. Under SPS, this allocation is FIXED for the entire grant duration — digest packets still reserve the same resources.